## Slide 1
Slot No.: ____________
Inter-University Avishkar Research Convention: 2026-27
Category: Engineering & Technology
Level: UG
MineSafe
Intelligent Safety Gear Compliance, Health Monitoring and Navigation System for Underground Miners
No GPS
No internet
No new cabling
01
THE PROBLEM
Chart: Coal-mine deaths in India
| 2023 | 2024 | 2025
Deaths | 41 | 49 | 51
141
deaths, 2023–25
355
serious accidents
0
GPS or phone signal below ground
In every rescue: nobody knows who is underground, where, or whether they are alive.
02
OBJECTIVES
Kit compliance
RFID / ID card + YOLOv8 photo check at the gate
Health
heart rate, SpO₂, temperature, falls, no-movement
GPS-free location
steps + heading, corrected at every repeater
Self-healing network
hop-by-hop ESP-NOW, no cabling or internet
Gas and heat
CH₄, CO, H₂S, wet-bulb at every repeater
Low cost
< ₹7,000 / repeater · ≈ ₹12,800 / suit
03
RESEARCH GAP
System | Kit | Vitals | Fall | Location | Gas | Price
MineGuard 360 | ✗ | ✓ | ~ | ~ | ✓ | quote
MineARC GuardIAN | ✗ | ✗ | ~ | zone | ✓ | quote
Leantegra UWB | ✗ | ✗ | ✗ | ✓ | ✓ | quote
Rajant Health | tag | ✓ | ✓ | ~ | ~ | quote
SmartKavach | ✗ | ~ | ✓ | ✗ | ✗ | quote
36Zero + Bodytrak | ~ | ✓ | ✓ | ✗ | ✗ | quote
MineSafe | ✓ | ✓ | ✓ | ✓ | ✓ | ₹12.8k
Novelty: the first low-cost system that combines kit check, vitals and GPS-free location in one self-healing network.
04
METHODOLOGY — ARCHITECTURE AND DATA FLOW
Smart suit
4 pods: vitals, fall, kit, steps
REP-03
gas · air · exit sign
REP-02
gas · air · exit sign
REP-01
main repeater
Hub laptop
API · AI kit check · evacuation planner
3D control app
browser or phone, live
ESP-NOW
ESP-NOW
ESP-NOW
Wi-Fi
Wi-Fi
alerts and evacuation routes return down the same chain · 1 packet / s per worker · data stays on site, no cloud
WORKER'S SHIFT
Kit up
suit self-checks
Entry check
ID card + YOLOv8 photo
Kit OK?
Underground
vitals · steps · gas, every 1 s
Alarm?
Alert + route
exit signs, cuff, helmet voice
Exit scan
dock charges
yes
yes
no → rejected, fix kit
no → keep monitoring
05
V4 SMART SUIT
Helmet pod
antenna at head height, voice alerts, helmet-on switch
Core pod · chest
ESP32-C6, 3000 mAh, IMU + pressure, SOS
Zip + seams
reed switch, conductive thread: opened or torn = alert
Wrist cuff
screen, 3 glove buttons, vibration, HR + SpO₂
Reflective bands
hi-vis in cap-lamp light
Boot pod
foot IMU measures every real stride
Never locked: removal is detected, never prevented
06
LOCATION WITHOUT GPS
1
Count steps
stride × gyro heading; pressure gives the level
2
Snap to tunnel
position pulled onto the mine-map centre line
3
Reset at repeater
signal ≥ −55 dBm → drift back to zero
4
Route around danger
Dijkstra from all exits, hazard zone ×1000 cost
Live 3D control app: routes bend around a gas leak, every exit sign updates
07
REPEATER: BUILT FOR THE MINE
CH₄ port on top
methane rises; rain chimney
LED exit sign
arrow + metres, under a drip hood
IP65 gasket
silicone cord, 6 × M4
85 dB buzzer
works if the hub is down
Guarded SOS
glove-sized, knock-proof
CO / H₂S below
heavier gases; flame arrestors
08
ELECTRICAL DESIGN AND PCBS
Mine 9–30 V
Battery 12 V
Diode OR
no reset
Fuse + TVS
1.6 A · 36 V
5 V buck
2 A, 90 %
XIAO · 3 MQ · matrix
≈ 3.7 W
Repeater
Core
Cuff
Helmet
Boot
5 own 2-layer boards · KiCad + Freerouting · 100 % routed · 0 unconnected pads
09
ENERGY BUDGET
Chart: 
| Repeater backup | Core pod | Helmet pod* | Boot pod*
Hours | 7 | 21 | 56 | 92
Hours on one charge; a shift is 12 h. *duty-cycled radio. Repeater ≈ 3.7 W on mine power.
10
COST
Chart: 
| Core pod | Helmet pod | Wrist cuff | Boot pod | Fabric + sensing
Suit cost | 2790 | 2260 | 1480 | 3270 | 3040
₹12.8k
per suit
Boot pod
3,270
Fabric + sensing
3,040
Core pod
2,790
Helmet pod
2,260
Wrist cuff
1,480
₹6,862 / repeater · ₹3.26 L for 10 repeaters + 20 suits
11
VALIDATION
Test | Pass criterion | Status
PCB DRC, 5 boards | 0 unconnected pads | Passed
CAD fit, 5 cases | no collisions | Passed
Power budget | core pod ≥ 12 h (21 h) | Passed
Repeater chain | self-forms, 3 / 3 | Passed
Gas + local buzzer | alarm at limit | Passed
Distance error | ≤ 5 % over 100 m | In progress
Alert latency | ≤ 3 s for 95 % | Planned
Fall detection | ≥ 90 %, ≤ 1 false / h | Planned
12
CONCLUSION
Every worker checked, monitored, located and reachable for the whole shift, on hardware a small mine can install itself.
Working V3 prototype: 3 repeaters, body unit, hub, 3D app
V4: 5 PCBs, 5 mine-rated cases, smart suit
Next: LoRa backbone, certified gas sensors, mine trial
SDG 3
Good health
SDG 8
Decent work
SDG 9
Industry
References [1] Ministry of Mines data, ETV Bharat, Aug 2026 · [2] Coal Mines Regulations 2017, reg. 153 · [3] NIOSH Pocket Guide to Chemical Hazards · [4] Bandyopadhyay et al., Wireless Information and Safety System for Mines, JSIR 2009 · [5] IMU-assisted UWB positioning in underground coal mines, Micromachines 2023 · [6] Real-time PPE compliance detection (YOLO), Sustainability 2023