## Slide 1: MineSafe
Intelligent Safety Gear Compliance, Health Monitoring and Navigation System for Underground Miners
Slot No.: ________
Category: Engineering and Technology · UG
Notes: 0:00–0:15. Slot number only — do not say your name or college. First-slide fields must match Annexure 2 of the MU Aavishkar rules; adjust if your coordinator gives a different format. The suit on the right is a live 3D model: click and drag to turn it.

## Slide 2: Underground, nobody knows who is where or if they are alive
141
deaths in Indian coal mines, 2023–25
355
serious accidents in the same period
0
GPS or mobile signal underground
SLBC tunnel, Telangana · 2025
8 trapped — radar needed to find them
Umrangso, Assam · 2025
flooded mine, 150+ hour search
Kolihan, Rajasthan · 2024
cage rope snapped, 15 trapped, 1 died
Ksan, Meghalaya · 2018
15 trapped, about 80-day search
Manual kit checks at the gate · no health monitoring · gas measured at a few points · evacuation by siren
Notes: 0:15–0:50. Source: Ministry of Mines data (ETV Bharat, Aug 2026). Every rescue shows the same gap: no last known position, no vitals, no way to tell each worker which way to go.

## Slide 3: No system combines kit check, vitals and GPS-free location
Product | Kit check | Vitals | Fall alert | GPS-free location | Gas | Public price
Teknovate MineGuard 360 | ✗ | ✓ | ~ | ~ | ✓ | ✗
MineARC GuardIAN | ✗ | ✗ | ~ | zone | ✓ | ✗
Leantegra (UWB) | ✗ | ✗ | ✗ | ✓ | ✓ | ✗
Rajant Health | tag | ✓ | ✓ | ~ | ~ | ✗
EasyM2M SmartKavach | ✗ | ~ | ✓ | ✗ | ✗ | ✗
36Zero + Bodytrak | ~ | ✓ | ✓ | ✗ | ✗ | ✗
MineSafe | ✓ | ✓ | ✓ | ✓ | ✓ | ₹6.9k / ₹12.8k
What is new: one integrated network · location without GPS or new infrastructure · repeaters that are also exit signs · a suit that checks the kit all shift · enterprise features at small-mine prices
Notes: 0:50–1:20. Nine commercial products checked (July 2026). Do not claim to beat Leantegra on positioning — the point is the integration and the cost.

## Slide 4: One self-healing network from the gate to the control room
Smart suit
core, helmet, cuff and boot pods — vitals, fall, kit, steps
REP-03
gas · air · exit sign
REP-02
gas · air · exit sign
REP-01
main repeater
Control-room hub
API · AI kit check · map · evacuation planner
ESP-NOW, 1 packet / s, hop by hop
Wi-Fi
alerts and evacuation routes ride back down the chain
Entry station
RFID / ID card + AI photo check
3D control app
browser or phone, live
Wi-Fi: kit verdict and pairing
No GPS, no internet, no cabling
radio chain forms and heals by itself
Every repeater measures gas
CH₄ top, CO / H₂S bottom, air + wet-bulb
One dashboard
who is underground, where, and how they are
Notes: 1:20–1:50. Walk the arrows left to right, then the dashed return path.

## Slide 5: Location without GPS, evacuation without guesswork
1
Count steps
steps × step length along the gyro heading; pressure gives the level
2
Snap to the tunnel
every position is pulled onto the nearest tunnel on the mine map
3
Reset at repeaters
strong signal (≥ −55 dBm) = next to that repeater: drift goes to zero
4
Route around danger
Dijkstra from all exits; tunnels in the hazard zone cost 1000×; each exit sign shows its arrow + distance
Live 3D control room during an evacuation: routes go around the gas leak, exit signs update
Notes: 1:50–2:20. Integrating acceleration drifts ~175 m a minute — that is why we count steps and reset at every repeater. V4 adds a foot IMU that measures each real stride.

## Slide 6: Designed for dust, water, methane, heat and blasting
Water and dust
IP65 gasket, drip hood, every opening faces down
Methane rises
CH₄ port on top under a rain chimney; H₂S / CO ports at the bottom
Ignition risk
sintered flame-arrestor seat at every gas port
Heat 30–45 °C
air sensor in its own chamber, away from heaters
Blasting shock
screw bosses, latching connectors, rubber grommets
Power cuts
mine supply + battery, switch-over with no reset
Dark and smoke
LED exit signs, reflective hi-vis tape
Thick gloves
16–22 mm buttons, vibration and voice alerts
Notes: 2:20–2:50. Every hardware decision starts from a mine condition. The suit is never locked — removal is detected, never prevented.

## Slide 7: Each repeater is a radio relay, gas station and exit sign
3D model — click and drag to turn it
Gas
MQ-4 CH₄ (top) · MQ-7 CO · MQ-136 H₂S (bottom), alarms to Indian limits
Air
temperature, humidity, wet-bulb heat limit 30.5 / 33.5 °C
Exit sign
8×32 LED matrix: arrow + distance to the safe exit
Alarm
85 dB buzzer works even if the control room is down
Power
9–30 V mine supply or battery, ≈ 3.7 W, ≈ 7 h backup
Case
223 × 292 × 118 mm, IP65 target, rock-bolt / chain mount
Notes: 2:50–3:30. Turn the 3D model to show the CH4 chimney on top and the downward-facing ports. Same board runs as main repeater or tunnel repeater.

## Slide 8: Five own PCBs: 100 % routed, 0 design-rule errors
Repeater schematic and board (100 × 75 mm)
2-layer, through-hole
hand-solderable, modules on sockets
Diode-OR power
fuse + TVS + 5 V / 2 A switcher
Suit boards
core 66 × 54 · cuff 46 × 42 · helmet 44 × 48 · boot 34 × 42 mm
KiCad 7 + Freerouting, generated by our own script: place, route, ground pour, DRC, Gerbers
Notes: 3:30–4:00. Point at the power path: mine supply and battery OR-ed by diodes, so a power cut never resets the repeater.

## Slide 9: V4 smart suit: the kit checks itself all shift
Core pod · chest
ESP32-C6, 3000 mAh, motion + pressure, guarded SOS
Helmet pod
antenna at head height, voice alerts, helmet-on switch
Wrist cuff
screen, 3 glove buttons, vibration, heart rate + SpO₂
Boot pod
foot IMU measures each real stride, heel force sensor
Seams and zip
conductive thread + zip switch: torn or opened = alert
Never locked: removal or a tear is detected and reported, never prevented
Notes: 4:00–4:30. Turn the suit to show the helmet pod at the back and the boot pod on the right heel. Helmet and boot talk to the core over ESP-NOW; only the cuff is wired.

## Slide 10: Four pods, each designed around its own board
Core pod
118 × 93 × 44 mm
Wrist cuff
88 × 75 × 27 mm
Helmet pod
75 × 66 × 31 mm
Boot pod
57 × 58 × 29 mm
Notes: 4:30–4:50. Lids shown lifted so the board, battery and modules are visible. Every case was fit-checked in CAD against its real KiCad board.

## Slide 11: Energy budget: the core pod lasts almost two shifts
Chart: Hours on one charge (shift = 12 h)
| Repeater backup | Core pod | Helmet pod* | Boot pod*
Battery life (h) | 7 | 21 | 56 | 92
* with the radio duty-cycled (V4 firmware). Datasheet estimates, to be confirmed by measurement.
ESP32-C6 (XIAO)
Wi-Fi, BLE, Zigbee + ESP-NOW on one 21 mm board
ESP-NOW, not Zigbee
no re-joining for a moving worker; LoRa later for long tunnels
Step counting, not UWB
UWB ≈ ₹2,000 per tag and anchor; steps cost nothing
Switching regulators
a linear 7805 would waste ≈ 11 W at 24 V
Gas on repeaters only
MQ heaters use 150 mA — wrong for a battery wearable
Notes: 4:50–5:15. Repeater: ≈ 3.7 W, mostly the three gas-sensor heaters. Core pod: ≈ 112 mA at 3.3 V → ≈ 21 h from 3000 mAh.

## Slide 12: Validated in steps: design and bench done, field tests next
Design checks
4 / 4 passed
PCB DRC: 0 unconnected pads (5 boards)
CAD fit check: no collisions (5 cases)
Power budget: core pod 21 h ≥ 12 h
Signal levels: ADC and 5 V logic in range
Bench tests
5 / 6 passed
Repeater chain forms by itself (3/3)
Air sensing logged (31.3 °C, 62 % RH)
Gas alarm + local buzzer
Hub logic + robustness with simulator
Body sensors: wiring being fixed
Field tests (pass criteria)
in progress
Alert to deepest worker ≤ 3 s (95 %)
Distance error ≤ 5 % over 100 m
Falls detected ≥ 90 %, ≤ 1 false / h
HR ± 5 bpm, SpO₂ ± 3 % vs oximeter
Hose test 30 min, 1 m drop, 24 h at 45 °C
Notes: 5:15–5:50. Be honest: V3 is in field calibration. Each field test has a numeric pass criterion; results are logged with screenshots and video.

## Slide 13: Affordable for small mines: checked, located, reachable
₹6,860
per repeater (PCB + mine case)
₹12,800
per smart suit
₹3.3 L
site: 10 repeaters + 20 suits
Every commercial system: enterprise quote only
Social
faster rescue with a last known position; falls, gas and heat caught as they happen
SDGs
3 Good health · 8 Decent work · 9 Industry and innovation
Next
LoRa backbone · certified NDIR / electrochemical gas sensors · intrinsic-safety design · field trial with a mine
Thank you
Notes: 5:50–6:30. End on cost and impact (20 of 100 marks are economic efficiency and social relevance). Stop by 6:45 — over 7:15 disqualifies.